## Slide 1: Project initiation document
KEECO
Knowledgeable Ecosystem for Establishment Control Objects
25th, December 2018.
V1.0
edited by /u/litechniks

## Slide 2: Vision
To create an open source home automation framework that provides a user-friendly application deployment to end nodes and an off-the-shelf control and monitoring server
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.

## Slide 3: Key aspects
For users:
Open source (GPL)
Low-cost HW support
Usage requires little to no programming knowledge
Web-based UI
Supports standard accessories
For programmers:
Ready to use automation framework
Open software interfaces on nodes and server side
Extensible node personalities
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.

## Slide 4: System Elements
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.
End Node
WEMOS
Ethernet or WiFi Enabled Arduino
Other devices in the future
Server
Raspberry
PC and other devices in the future
User Client
Any device with a modern web browser

## Slide 5
Initial Node Setup
  Connected to PC via USB
  Node HW type, Personalities, I/O assignment, Update rates, Network connection data, Autonomous I/O Handling is configured by user on GUI running on/connected to the Server
  Application is built and deployed to the Node with a UUID from the GUI. Option to export code for programmers.
  Node characteristics assigned to UUID stored on Server
  Node later can be updated OTA
On Connection
  Node checks in at known Server IP and announces personalities (to double-check with Server and for Direct Access)
  Temporary Data Historian data to be uploaded to Server
  Outputs: send last set values to Server. Inputs: send actual values to server
Connected
  Inputs: sent to server periodically (update rate) or on-change.
  Outputs: changed when received new value
  Autonomous I/O handling
Disconnected
  Autonomous I/O handling
  Data stored in Temporary Data Historian
  Try to connect to server – with timeout
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.
End Node
Personalities (can be multiple):
Digital Input
Digital Output
Analog Inout
Analog Output
Misc
Functions
I/O Handling
Communication to Server
Temp. Data Historian
Autonomous I/O Handling
Interface for Extension
Access
via Server
Direct – configuration and debug
System Elements – Node Detailed

## Slide 6: System Elements - Detailed
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.
End Node
Personalities (can be multiple):
Digital Input
Digital Output
Analog Inout
Analog Output
Misc
Functions
I/O Handling