## Slide 1: Project initiation document
KEECO
Knowledgeable Ecosystem for Establishment Control Objects
25th, December 2018.
V1.0
edited by /u/litechniks

## Slide 2: Vision
To create an open source home automation framework that provides a user-friendly application deployment to end nodes and an off-the-shelf control and monitoring server
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.

## Slide 3: Key aspects
For users:
Open source (GPL)
Low-cost HW support
Usage requires little to no programming knowledge
Web-based UI
Supports standard accessories
For programmers:
Ready to use automation framework
Open software interfaces on nodes and server side
  Abstraction layers
  Mainstream internet technologies
Extensible node personalities
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.

## Slide 4: System Elements
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.
End Node
WEMOS
Ethernet or WiFi Enabled Arduino
Other devices in the future
Server
Raspberry
PC and other devices in the future
User Client
Any device with a modern web browser
HTTP/WebSockets
HTTP

## Slide 5
Initial Node Setup
  Connected to PC via USB
  Node HW type, Personalities, I/O assignment, Update rates, Network connection data, Autonomous I/O Handling is configured by user on GUI running on/connected to the Server
  Application is built and deployed to the Node with a UUID from the GUI. Option to export code for programmers.
  Node characteristics assigned to UUID stored on Server
  Node later can be updated OTA
On Connection
  Node checks in at known Server IP and announces personalities (to double-check with Server and for Direct Access)
  Temporary Data Historian data to be uploaded to Server
  Outputs: send last set values to Server. Inputs: send actual values to server
Connected
  Inputs: sent to server periodically (update rate) or on-change.
  Outputs: changed when received new value
  Autonomous I/O handling
Disconnected
  Autonomous I/O handling
  Data stored in Temporary Data Historian
  Try to connect to server – with timeout
WebServer
  For Direct Access simplified GUI
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.
End Node
Personality Classes (can be multiple):
Digital Input
Digital Output
Analog Inout
Analog Output
Misc
Functions
I/O Handling
Communication to Server
Temp. Data Historian
Autonomous I/O Handling
Interface for Extension
Simple WebServer
Access
via Server
Direct – configuration and debug
System Elements – Node Detailed

## Slide 6
Server DataBase
  SQL DataBase to store Input/Output Data
  User Authentication actions
  Node list and capabilities
  Can be accessed by both the Automation Server and WebServer (read-only, performance reasons and extendibility)
Automation Server
  Has no built-in GUI. Communicates with the WebServer via WebSockets to provide web-based GUI.
  Can merge Arduino code templates and can communicate with Arduino IDE CLI installed on Raspberry or PC to build and deploy applications to Nodes
  Maintains a database of Nodes and their personalities based in user configuration
  Handles WebSocket connections to Nodes
  Handles WebSocket connections to WebServer
  Task Scheduler to be able to schedule changes on Outputs
  I/O Relations – basic logical relations between multiple Inputs/Outputs
  WebSocket based API for I/O Relations for future extensions (machine learning, etc…)
WebServer
  Provides User Authentication
  WebSocket Interface to Automation Server
  Provides GUI for Automation Server
  Interface to SQL DataBase to retrieve historical data
GUI on Server
  Can be viewed in web browser, same as the GUI can be viewed on clients
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.
System Elements – Server Detailed
Server
WebServer
User Authentication
Interface to Automation Server
Interface to DataBase
Provide Application and Configuration GUI
Automation Server
Initial setup of Nodes
Accepting connections from Nodes
Handling data to/from Nodes
Storing data in Server DataBase
Interface to WebServer
Task Scheduler. I/O Relations
GUI
Same GUI as on User Clients (in Browser)
Server DataBase
Periodic and event-triggered data
User authentication log
List of configured Nodes

## Slide 7: System Elements - Communications
KEECO Knowledgeable Ecosystem for Establishment Control Objects | Project initiation document v 1.0 | 25th, December 2018.
User Client
End Node
Node Functionality
Simple WebServer
WebSockets
Server
WebServer
User Authentication
Interface to Automation Server
Interface to DataBase
Provide Application and Configuration GUI
Automation Server
Initial setup of Nodes
Accepting connections from Nodes
Handling data to/from Nodes
Storing data in Server DataBase
Interface to WebServer
Task Scheduler. I/O Relations
GUI
Same GUI as on User Clients (in Browser)
Server DataBase
Periodic and event-triggered data
User authentication log
List of configured Nodes
WebSockets
Configuration & Actual Values: JSON
Historical Data: Binary
SQL Connection
SQL
Connection
WebSocket
HTTP
HTTP